## Slide 1
iSupport Platform
For your daily care
Team members:
Burdisso Sara s275424
Centonze Ilenia s277389
Ferrara Mauro s276932
Pasotti Andrea s275100
Notes: Welcome to iSupport Platform
iSupport platform aims to help in monitoring patients (peiscens) in a depressed state or suspected ones.

## Slide 2: The idea - overview
Recording and analyzing data from sensors
Emergency management
Remote Patient Monitoring
Objective:
To help clinicians and caregivers follow individuals in depressive states during their treatment period by providing a remote monitoring and support platform.

## Slide 3: Protocolli di Comunicazione
MQTT
Lightweight and flexible protocol suitable for ioT applications.
Publish messages in JSON format using QoS 2
Receive messages using QoS 2
Message topic: hierarchical, containing patient information
REST Web Service
It allows to synchronize the communication between the parties.
Catalog: accesses the system information present in a JSON file and communicates it to the other actors;
ThingSpeak: database with data coming from the sensors. The data is accessed with a GET request and provided via a message in JSON format.

## Slide 4: Use Case Diagram - proposal
Patient Control
Device Connector
Telegram Bot
Node-RED
Message Broker
Microservices
User Awareness
Home System Control
Data Analysis
Light Shift
ThingSpeak platform
ThingSpeak Adaptor
Legend:
MQTT Communication
REST Web Services (provider)
REST Web Services (consumer)
Catalog

## Slide 5: Use Case Diagram - modified
Patient Control
Device Connector
Node-RED
Telegram Bot
Message Broker
Microservices
User Awareness
Home System Control
Data Analysis
Light Shift
ThingSpeak platform
ThingSpeak Adaptor
Legend:
MQTT Communication
REST Web Services (provider)
REST Web Services (consumer)
Catalog

## Slide 6: Catalog
It communicates with all the other actors in the platform exploiting REST communication.
{
"Catalog_url":"http://127.0.0.1:8080",
"baseTopic":"iSupport/",
" LightShift ":{
"clientID" : "LigthShiftMS",
"endTopic":[" actuators/Light"]
},
...

## Slide 7: Catalog
{
"broker": {
"IPaddress": "test.mosquitto.org",
"port": 1883
},
"token": "1711013176:AAH6bCdvA0dOdL8fX4FIfCPGEqpEFNjN1d4",
"deviceList": [
{
"deviceName": "smartwatch_1",
"deviceID": "1",
"measureType": [
"HeartRate",
"Accelerometer"
],
"availableServices": [
"MQTT"
],
"servicesDetails": [
{
"serviceType": "MQTT",
"topic": [
"iSupport/1/sensors/Body"
]
}
],
"lastUpdate": 1621764472.704841
}],
"patientList": [
{
"patientID": "1",
"patientName": "Mario",
"patientSurname": "Rossi",
"LightsSchedule": "7:30-8:30",
"connectedDevices": [
{
"measure": [
"Heart Rate",
"Acceration"
],
"deviceID": "smartwatch_1"
},
"telegramIDs": [1234567],
"thingspeakInfo": {
"apikeys": [
"ZQ2AJZABDSC4MXXG",
"SV1HOET58CE7225M"
],
"channel": 1342741
},
"lastUpdate": 1622981412.5148401
}
]
}
Catalog.json contains information about general configuration, registered devices and registered patients.

## Slide 8: Catalog
It communicates with all the other actors in the platform exploiting REST communication.
It has 3 main functions:
  Retrieve (GET)
  Add (POST)
  Update (PUT)
GET
IP/broker
IP/token
IP/patients
IP/devices
IP/deviceID/ID
IP/patientID/ID

## Slide 9: Catalog
It communicates with all the other actors in the platform exploiting REST communication.
It has 3 main functions :
  Retrieve (GET)
  Add (POST)
  Update (PUT)
POST
IP/device
IP/patient
IP/chatID/ID
Body={
"chatID": 1234567,
}
Body={
"patientID": "2",
"patientName": "Francesco",
"patientSurname": "Bianchi",
"LightsSchedule": "17:00-18:30"
}
Body={
"deviceName": "mot_1",
"deviceID": "3",
"measureType": [
"Motion"
],
"availableServices": [
"MQTT"
],
"servicesDetails": [
{
"serviceType": "MQTT",
"topic": [
"iSupport/1/sensors/Motion"
]
}
]
}

## Slide 10: Catalog
It communicates with all the other actors in the platform exploiting REST communication.
It has 3 main functions:
  Retrieve (GET)
  Add (POST)
  Update (PUT)
PUT
Body={
"patientID": «1",
"patientName": "Francesco",
"patientSurname": "Bianchi",
"LightsSchedule": "17:00-18:30",
"connectedDevices": [
{
"measure": "Temperature",
"deviceID": "t_1"
}
],
"telegramIDs": [],
"thingspeakInfo": {
"apikeys": [
"ZQ2AJZABDSC4MXXG",
"SV1HOET58CE7225M"
],
"channel": 1342741
},
"lastUpdate": ""
}
IP/patient
IP/device
Body={
"deviceName": "smartwatch_1",
"deviceID": "1",
"measureType": [
"HeartRate",
"Accelerometer"
],
"availableServices": [
"MQTT"
],
"servicesDetails": [
{
"serviceType": "MQTT",
"topic": [
"iSupport/1/sensors/Body"
]
}
],
"lastUpdate": 1623097970.3872042
}

## Slide 11: Catalog
Start
Delete the device from «DeviceList»
Catalog keeps updated the “deviceList” with the devices correctly connected and removes all the devices that are disconnected.
Check all «LastUpdate»
«LastUpdate» >120 s
Yes
No
Wait for 60 seconds
"deviceList": [
{
"deviceName": "smartwatch_1",
"deviceID": "1",
"measureType": [
"HeartRate",
"Accelerometer"
],
"availableServices": [
"MQTT"
],
"servicesDetails": [
{
"serviceType": "MQTT",
"topic": [
"iSupport/1/sensors/Body"
]
}
],
"lastUpdate": 1621764472.704841
}]

## Slide 12: Device Connector
Temperature and Humidity:
Extraction of a value from uniform distributions that have specific limits that change according to the month in which publication occurs. User sets mode of generation:
  in the suitable range
  out of range
Motion Sensor:
It is a value (1/0) set by the user
Devices implemented in the simulation:
- Temperature and humidity sensors
Morion Sensor
Heart rate sensor
Accelerometer sensor
Actuator for air Conditionair system
Smart light bulb actuator

## Slide 13: Device Connector
-HR and Accelerometer measurments:
Accelerometer measurments are obtained from 2 database: REST.txt and SPORT.txt
REST configuration
Devices implemented in the simulation:
- Temperature and humidity sensors
Motion Sensor
Heart rate sensor
Accelerometer sensor
Actuator for air Conditionair system
Smart light bulb actuator
REST.txt
0.06275
0.04957
0.11802
0.28902
0.10596
0.556840…
+
HR
bpm

## Slide 14: Device Connector
Devices implemented in the simulation:
- Temperature and humidity sensors
Motion Sensor
Heart rate sensor
Accelerometer sensor
Actuator for air Conditionair system
Smart light bulb actuator
SPORT.txt
6.920512
7.049275
7.176033
7.291157
7.398414
8.597905
8.611896…
+
HR
bpm
-HR and Accelerometer measurments:
Accelerometer measurments are obtained from 2 database: REST.txt and SPORT.txt
Sport configuration

## Slide 15: Device Connector
Devices implemented in the simulation:
- Temperature and humidity sensors
Motion Sensor
Heart rate sensor
Accelerometer sensor
Actuator for air Conditionair system
Smart light bulb actuator
REST.txt
0.06275
0.04957
0.11802
0.28902
0.10596
0.556840…
+
HR
bpm
-HR and Accelerometer measurments:
Accelerometer measurments are obtained from 2 database: REST.txt and SPORT.txt
«Danger» configuration

## Slide 16: Device Connector
Actuation Commands:
Switching on the air Conditionair system to maintain optimal temperature and humidity levels.
Switching on smart lights to enable luminotherapy.
Devices implemented in the simulation:
- Temperature and humidity sensors
Presence Sensor
Heart rate sensor
Accelerometer sensor
Actuator for air Conditionair system
Smart light bulb actuator

## Slide 17: Device Connector
Catalog: to register devices or refresh registration with a REST communication.
ThingSpeak Adaptor: which receives all measurements from the sensors published by Device Connector.
Home system Control: device connector publishes sensor measurements to this microservice, which sends actuation commands to switch on and off the temperature control system.
Light Shift: from which device connector receives actuation command to switch on/off smart light bulbs for luminotherapy.
Communication with
self.__message={
"bn": 1,
"e": [{
"n": "Heart Rate",
"value": 61,
"timestamp": "123456",
"u": "bpm"
},
{
"n": "Accelerometer",
"value": 0.060369,
"timestamp": "123456",
"u": "m/s2"
}
]
}
Communication with the other actors is done using SenML format.

## Slide 18: Patient Control
How it works
Analyze heart rate and acceleration data
Communication with
ThingSpeak: for getting measurement of 10 minutes windows.
Goal: Monitoring the patient and detecting of panic attack

## Slide 19: Patient Control
How it works
Analyze heart rate and acceleration data
Communicate an alert in case of panic attack to the doctor and caregiver
Communication with
ThingSpeak: for getting measurement of 10 minutes windows.
ThingSpeak: for recording the panic attack event
Telegram bot: for communicating the panic attack event

## Slide 20: Home system Control
How it works
Manages temperature and humidity inside the house
Verifies patient presence in the home
Avoid wasting energy by establishing activation time slots
Start
Receives data from sensors
Control Strategy every 10 minutes
Goal: Monitoring home for having a comfortable enviroment

## Slide 21: Home system Control
How it works
Start
Receives data from sensors
Control Strategy every 10 minutes
Check Temperature and Humidity window
Temperature out of range
Humidity out of range
Presence + time slots
Yes
Yes
Yes
No
No
No
Air Conditioning System
ON
Air Conditioning System
OFF
Manages temperature and humidity inside the house
Verifies patient presence in the home
Avoid wasting energy by establishing activation time slots

## Slide 22: Home system Control
How it works
Communication with
Device connector:
  Continuously receives data from Temperature and Humidity sensors
  Sends actuation commands if it is identified a condition to switch ON or OFF the Air Conditioning System
Manages temperature and humidity inside the house
Verifies patient presence in the home
Avoid wasting energy by establishing activation time slots

## Slide 23: Light Shift
Manages the lighting system in relation to the physician's established schedule for luminotherapy
Catalog:
  to obtain the times in which to activate the luminotherapy
Device Connectors:
  to send actuations commands to turn the lights ON or OFF
How it works
Communication with

## Slide 24: ThingSpeak
It’s a platform used like a database in which there are all measurement got from different sensors implemented on iSupport platform
It uses an adaptor ThingSpeak Adaptor which:
Allows you to implement communication via MQTT.
Increases the scalability of the platform
Increases interoperability between components.

## Slide 25: ThingSpeak third part Application User Interface

## Slide 26: ThingSpeak
It’s a platform used like a database in which there are all measurement got from different sensors implemented on iSupport platform
It uses an adaptor ThingSpeak Adaptor which:
Allows you to implement communication via MQTT.
Increases the scalability of the platform
Increases interoperability between components.
Communication with
Device Connector: continous updating of measurements
Data Analysis: sending measurements received from the device connector.
Patient Control: sending measurements related to specific observation windows.

## Slide 27: Data Analysis
How it works
Process patient measurements to get weekly or monthly statistics:
  Weekly report about average heart rate in 3 time bands.
  Weekly report about patient’s activity status (percentage of low, medium, high intensity obtained as comparing rate and acceleration measurements
  Number of monthly panic attacks
  Weekly report about how much time patient spends in the bedroom (level of sedentary lifestyle)
Communication with
ThingSpeak Adaptor: to get measurements
Node-RED: to create statistical graphs
Node-RED interface

## Slide 28: Data Analysis
How it works
Process patient measurements to get weekly or monthly statistics:
  Weekly report about average frequency values in 3 time bands.
  Weekly report about patient’s activity status (percentage of low, medium, high intensity obtained as comparing rate and acceleration measurements.
  Number of monthly panic attacks.
  Weekly report about how much time patient spends in the bedroom (level of sedentary lifestyle).
Communication with
ThingSpeak Adaptor: to get measurements
Node-RED: to create statistical graphs
Node-RED interface

## Slide 29: Data Analysis
How it works
Process patient measurements to get weekly or monthly statistics:
  Weekly report about average frequency values in 3 time bands.
  Weekly report about patient’s activity status (percentage of low, medium, high intensity obtained as comparing rate and acceleration measurements.
  Number of monthly panic attacks.
  Weekly report about how much time patient spends in the bedroom (level of sedentary lifestyle).
Communication with
ThingSpeak Adaptor: to get measurements
Node-RED: to create statistical graphs
Node-RED interface

## Slide 30: Node-RED
How it works
Nodes:
  MQTT communication node
  Python function
  Two blocks to visualize msg.payload in debug display
  A rbe block
  A digital display and three chart

## Slide 31: Telegram Bot
‘/start’ function:
  Telegram user registration on platform
‘/status’ function:
  Visualization of ThingSpeak graphs about vital signs
Emergency management:
  Getting alert message from the Patient Control microservice in case of Panic Attack.
Emergency management
Allow the doctor and the caregiver to always be updated on the Heart Rate, Movement and Recurrence trends of panic attacks.

## Slide 32: Telegram Bot
‘/start’ function:
  Telegram user registration on platform
Emergency management
Allow the doctor and the caregiver to always be updated on the Heart Rate, Movement and Recurrence trends of panic attacks.
Notes: Collega la chatID del medico e caregiver al paziente

## Slide 33: Telegram Bot
‘/status’ function:
  Visualization of ThingSpeak graphs about vital signs
Emergency management
Allow the doctor and the caregiver to always be updated on the Heart Rate, Movement and Recurrence trends of panic attacks.

## Slide 34: Telegram Bot
Emergency management:
  Getting alert message from the Patient Control microservice in case of Panic Attack.
Emergency management
Allow the doctor and the caregiver to always be updated on the Heart Rate, Movement and Recurrence trends of panic attacks.

## Slide 35: Telegram Bot
Emergency management
Allow the doctor and the caregiver to always be updated on the Heart Rate, Movement and Recurrence trends of panic attacks.
Communication with
Patient Control: which publishes a message to the telegram bot if it detects a panic attack
ThingSpeak: required for viewing graphs
Catalog: retrieve chatId and token

## Slide 36
Thanks for your attention
Team 3:
Burdisso Sara s275424
Centonze Ilenia s277389
Ferrara Mauro s276932
Pasotti Andrea s275100